## Slide 1: Critical Design Review USLI
Windward Community College
University of Hawaii
2012-2013

## Slide 2: Rocket: The Green Machine Payload: Wilfred
Ke Kime Kao Lele Keu Loa
Kristi Ross
Lyra Hancock
Warren Mamizuka
Ada Garcia
Kristin Barsoumian
Team Official: Dr. Jacob Hudson

## Slide 3: Rocket Design Criteria
Build a Rocket to be launched to an altitude of 5280 ft. (1 mile)
Rocket must carry a scientific payload
Rocket must return safely

## Slide 4: The Green Machine

## Slide 5: Flight Profile

## Slide 6: Rocket Design Details
Length: 124 in.
Diameter: 6 in.
Unloaded Weight: 496 oz.
Weight: 724 oz.
Materials: G10 Fiberglass
Recovery: Dual Deployment, Electronic
Propulsion: AEROTECH L1500T

## Slide 15: Motor Selection
AEROTECH L1500T
Total Impulse: 5120 Ns
Casing: 98/7680
Average Thrust: 1537 N
Peak Thrust: 2381 N
Burn Time: ~3.0 sec
Thrust to weight: ~7.4

## Slide 16: Flight Characteristics
GPS Flight in nose cone
Variable Drag Configuration (VDC)
Four-fin design
Avionics
Dual-Deployment
16

## Slide 17: Rocket Stability
Center of Pressure: 98.73 in.
Center of Gravity: 81.7 in.
Stability: 2.84
Rail Exit Velocity
-Rocket hits minimum safe speed (44 ft/s) at 68 in. during boost phase (before leaving rail).

## Slide 18: Variable Drag Configuration
Drag force is linear to ~30 degrees
Approximate altitude loss ~1.2%/degree
30 degree deployment yields ~36% loss
Must yield max altitude below 7180 ft. and above 5280 ft.

## Slide 19
Chart: Percent Altitude Lost vs. VDC Deployment Angle
| 0.0 | 5.0 | 10.0 | 13.0 | 15.0 | 20.0 | 24.0 | 25.0 | 30.0 | 33.0 | 35.0 | 40.0
 | 2.33 | 4.65 | 11.6 | 7.75 | 12.4 | 19.1 | 17.8 | 24.5 | 14 | 30.3 | 36.7

## Slide 20: Descent: Parachutes
Drogue Chute
42 in. diameter
Deployed at apogee
Descent at 70ft/s
Main Chute
144 in. diameter
Deployed at 2500 ft.
Descent at 21 ft/s
*Chutes will be connected by 2-ton, 20ft. shock cords

## Slide 21: Descent: Kinetic Energy Calculations
Initial Descent Stage
KE = 3610 ft-lb
Final Descent Stage
Descending in three sections
KEA V= 61.6 ft-lb
KEBooster = 74.6 ft-lb
KENC/SMD = 53.5 ft-lb

## Slide 22: Wilfred
Arduino Nano
Magnetometer (3-axis)
Operational Amp
Micro-SD storage
Accelerometer (3-axis)

## Slide 23: Wilfred
Arduino Mega 2560
Xbee-Pro
BMP085 – Temperature, Pressure,
Altitude
DHT11 – Humidity
TSL2561 – Light Sensor
TTL Serial JPEG – Camera
Real time clock

## Slide 24: Timeline

## Slide 25: Important Dates
Rocket
Jan. 27 & Feb. 16- Subscale Testing
Feb. 23- Ejection Charge Test
Mar. 10- Full Scale Low Power

## Slide 26: Important Dates
Education Outreach
Sept. 29- WCC 12th Annual Ho’olaule’a
Oct. 28- Le Jardin Academy Business Fair
Nov. 10- Aerospace Flight Lab Gifted & Talented
Dec. 2- Kaneohe Christmas Parade
Dec. 3- American Cancer Society Family Camp
Jan. 19- Physics Olympics
Feb. 9- Wow! That’s Engineering!

## Slide 27
Acknowledgements:
Hawai’i Space Grant Consortium
Indigenous Knowledge in Engineering
Dr. Joe Ciotti
Dr. Jacob Hudson
Jim and Becky Green
Joleen Iwaniec