## Slide 1: Preliminary Design Review
Windward Community College
University of Hawaii
2012-2013

## Slide 2: Rocket: The Green Machine Payloads: Wilfred
Ke Kime Kao Lele Keu Loa
Kristi Ross
Lyra Hancock
Warren Mamizuka
Ada Garcia
Kristin Barsoumian
Team Official: Dr. Jacob Hudson

## Slide 3: Rocket Design Criteria
Build a Rocket to be launched to an altitude of 5280 ft. (1 mile)
Rocket must carry a scientific payload
Rocket must return safely

## Slide 4: The Green Machine

## Slide 5: Flight Profile

## Slide 6: Rocket Design Details
Length: 121”
Diameter: 6”
Unloaded Weight: 496 oz.
Weight: 724 oz.
Materials: G10 Fiberglass
Recovery: Dual Deployment, electronic
Propulsion: AEROTECH L1500T

## Slide 15: Characteristics
GPS Flight in nose cone
Variable Drag Configuration (VDC)
Four-fin design
Avionics
Dual deployment

## Slide 16: Rocket Stability
Center of Pressure: 94.4”
Center of Gravity: 81.7”
Stability: 2.12

## Slide 17: Motor Selection
AEROTECH L1500T
Total Impulse: 5120 Ns
Casing: 98/7680
Average Thrust: 1537 N
Peak Thrust: 2381 N
Burn Time: ~3.0 sec
Thrust to weight: ~7.44

## Slide 18: Variable Drag Configuration
Drag force is linear to ~30 degrees
Approximate altitude loss ~1.2%/degree
30 degree deployment yields ~36% loss
Must yield max altitude below 7180 ft and above 5280 ft

## Slide 19: Wilfred
Magnetometer (3-axis)
12-bit ADC
Operation Amp
Micro SD storage
Accelerometer (3-axis)

## Slide 20: Wilfred
Arduino Nano
Xbee-Pro
BMP085 – Temperature, Pressure, Altitude
DHT11 – Humidity
TSL2561 – Light Sensor
TTL Serial JPEG – Camera
Real time clock

## Slide 21: Timeline
Chart: 
| PDR | CDR | FRR | PLAR | Rocket Construction | Deployment Test | FSLP | Sensor Testing | Software Integration | (GND) Hardware Construction | (GND) Payload Testing | (FLY) Hardware Construction | (FLY) Payload Testing | Launch Day I | Launch Day II | Education Outreach | Le Jardin Academy Business Fair | Kaneohe Christmas Parade | American Cancer Society Family Camp
 | 39707 | 39767 | 39844 | 39927 | 39825 | 39866 | 39874 | 39707 | 39748 | 39748 | 39781 | 39818 | 39852 | 39755 | 39769 | 39748 | 39782 | 39783
 | 41 | 58 | 44 | 10 | 34 | 1 | 7 | 35 | 32 | 32 | 36 | 34 | 28 | 1 | 1 | 1 | 1 | 1

## Slide 22: Important Dates
Rocket
November 4 – Subscale testing
January 3 – Subscale testing
January 19 – Ejection Charge Test
March 10 - Full Scale Low Power
Education Outreach
October 28
December 1
December 2

## Slide 23
Acknowledgements:
Hawai’i NASA Space Grant Consortium
Indigenous Knowledge in Engineering
Dr. Joe Ciatti
Dr. Jacob Hudson
Jim and Becky Green